## Slide 1
CALSYS Upgrade
Darragh O’Donoghue
Why?
Unacceptably low light throughput resulting in loss of science time while getting wavelength calibrations
The existing system does not emulate the spherical aberration caustic of the primary mirror, as originally envisaged by A. Swat
The existing system has no imaging capability at all. It simply sprays a (small) amount of light at the telescope focal plane
There is a systematic wavelength calibration zero point error in F-P data

## Slide 2
Existing system vs ‘on sky’
Existing Calsys +SAC
Stars + Primary mirror + SAC
No 200 mm spherical aberration caustic
No imaging at all

## Slide 3
What will be upgraded?
Existing
system
Existing Calsys Optical
Relay System (CORS)
The contents of this is the ONLY thing that will be upgraded
SAC
SAC
Baffle
Lamp
Bay
Liquid
Light
Guides
Relay Optics (CORS)

## Slide 4
Fresnel Lens Optical Design
On-axis field angle only
All field angles

## Slide 5
Mechanical Schematic: Overall
On-axis field angle only
All field angles
Light guides
Fresnel lenses 3,2 and 1
Existing carbon fiber enclosure which will be re-used

## Slide 6
Budget
Fresnel Lenses: US$ 17820
Other optics: US$ 2400
Custom mechanical ZAR 24000 Grand Total: ZAR 289453 R300 000 + 20% contingency approved by the BEC on Friday
Schedule
Design phase complete 2 weeks
Fresnel Lens procurement: 10 weeks Other optics procurement Custom mechanical
Assembly & Test: 2 weeks
Installation: 2 days
Completion: 15 weeks